## Slide 1: Hyper-Specific Prefixes: Gotta Enjoy the Little Things in Interdomain Routing
Presenter: Khwaja Zubair Sediqi
23.May.2023
Authors: Khwaja Zubair Sediqi, Lars Prehn, Oliver Gasser
zsediqi@mpi-inf.mpg.de, lprehn@mpi-inf.mpg.de, oliver.gasser@mpi-inf.mpg.de
Paper Published at: ACM SIGCOMM Computer Communication Review, Volume 52 Issue 2, April 2022

## Slide 2: Introduction
﻿
ASes use the BGP to announce prefixes
BGP best practices recommend filtering prefixes
  more specific than /24 in IPv4 and /48 in IPv6
Plenty of /25 to /32 IPv4 and /49 to /128 IPv6 exist
hyper-specific prefixes (HSPs)
How prominent and why HSPs exist in the Internet routing ecosystem?

## Slide 3: Related Work
﻿In 2014 and 2015 Aben and Petrie
  announced /24, /25, and /28 IPv4 prefixes
  RIPE Atlas measurements
  HSPs visible at most 20 % of RIPE RIS peers
In 2017, Strowes and Petrie conclude
  at most one fourth of all BGP peers
In 2017, Huston analyzed different types of more-specific prefixes
hole punching (different origin AS),
traffic engineering (same origin AS, but different AS path),
overlay (same AS path)

## Slide 4
Methodology
ASDB
  ﻿ For our analysis we utilize “snapshots“ from the RC projects RIPE RIS , Routeviews, and Isolario
    From Jan.2010 to October.2021
    Quarterly, 7days per quarter
    BGP RIBs – every 24 hours
    BGP Updates – every 5 mins
    Applied filters to clean the data
    Supplemental datasets
Notes: Resource Public Key Infrastructure (RPKI) Snapshots:
  ROA records to validate the legitimate announcements of prefixes by ASes
Internet Routing Registries (IRRs) Snapshots:
  Records containing route-object information
AS Relationships Inferences (CAIDA)
AS Classification Inferences (CAIDA)

## Slide 5
﻿1. OBSERVABILITY

## Slide 6
HSPs in Routing Ecosystem
HSPs make ~ 14% to more than 20% of of all the prefixes
Share of HSPs in the Interent
HSPs make ~ 10% of all the prefixes
Notes: To understand the prevalence of hyper-specific prefixes, we aggregate the routing tables of all collector peers and compare the distribution of prefixes depending on CIDR sizes. The figure shows those distributions as stacked bar plots for each snapshot. We observe that up to 13 % (in 2015) and 25 % (in 2018) of totally visible prefixes are hyper-specific for IPv4 and IPv6, respectively. Yet, the usual contribution of HSPs is approximately 10 % for most months. Note that this does not mean that any single routing table contains that many HSPs on its own.
In summary, we observe that the presence of hyper- specific prefixes in the Internet’s routing ecosystem has in- creased through the last decade and HSPs make up about one-tenth of all the prefixes that are observed by route collec- tors. In IPv4 the increase in HSPs is driven by an increment in feeder ASes, whereas in IPv6 we see an increase also for a constant set of feeder ASes.

## Slide 7
HSP Visibility and Consistency
We use one year data of BGP RIBs and updates
to track every HSP for the whole year
There is a correlation between consistency and visibility
HSPs have life span from days to more than a year
Many have visibility to less than 50 peer ASes
Notes: To improve our understanding of this insight, we analyze the visibility of HSPs, i.e., by how many peers each HSPs is seen. At the same time, we want to understand what causes the substantial fluctuations in the number of HSPs; hence, we also analyze their consistency, i.e., the fraction of time for which the prefix was seen by at least one feeder AS. Given that a one-week observation period would not provide much insight into consistency patterns, we conduct this analysis using data from the entirety of 2020. We first read the RIB snapshots from January 1, 2020 and then apply all updates for the whole year sequentially. By tracking the state of each routing table on a per-update basis, we can extract consistency in seconds granularity.
Figure 2 reports the visibility of an HSP on the y-axis against its consistency on the x-axis. For both heatmaps— IPv4 (left) and IPv6 (right)—each cell represents groups of ten feeder ASes on the y-axis and two weeks of time on the x-axis. We first observe that there is no particular con- sistency trend: While some HSPs can only be observed for less than two weeks, others can be observed throughout the entire year. Our second observation is that the vast majority of hyper-specific prefixes can only be observed by a small number of collector peers, although we do also observe HSPs being visible during the entire year by hundreds of peers. This observation aligns with the restricted propagation char- acteristics of HSPs reported by previous blog posts [1, 2, 51] and observed by our own active experiments (an in-depth de- scription of the experiments, their analysis, and subsequent results can be found in Appendix D). We hypothesize that the substantial fluctuations in the number of totally observed HSPs is a result of these two observations; the restricted propagation of HSPs might inflate the importance of the individual placement of feeder ASes and HSP origin ASes, and the tens of thousand of short-lived HSPs might cluster around certain real-world events, such as DDoS attacks or data center outages.
While most HSPs only propagate locally, some of them are globally visible and can be consistently observed throughout an entire year.

## Slide 8
2. USE CASES & FUNCTIONS
Notes: Consider the following example: If an AS wants to defend one of its servers against an ongoing DDoS attack, it may use blackholing an- nouncements. Up to 98 % of these announcements are /32 (/128) IPv4 (IPv6) prefixes, i.e., they only cover the specific addresses of the attacked servers [9, 10, 15]. Larger CIDR sizes are rarely used for blackholing, as they would impair the services running on non-attacked servers as well, i.e., they would introduce unnecessary collateral damage [32].
In summary, we observe that for IPv4 many and for IPv6 some HSPs are likely related to blackholing activities due to the used HSP prefix size.
As our CIDR-based analysis only provides us with hints on the actual usage, we now also analyze the services hosted in hyper-specific prefixes.

## Slide 9
CIDR Sizes of HSPs
CIDR sizes hint use cases
  /32 and /128 for blackholing purposes
  /30, /29 peering subnets
  /56 and /64 address block assignments
  /25 traffic engineering
HSPs have heterogeneous use cases
Notes: Consider the following example: If an AS wants to defend one of its servers against an ongoing DDoS attack, it may use blackholing an- nouncements. Up to 98 % of these announcements are /32 (/128) IPv4 (IPv6) prefixes, i.e., they only cover the specific addresses of the attacked servers [9, 10, 15]. Larger CIDR sizes are rarely used for blackholing, as they would impair the services running on non-attacked servers as well, i.e., they would introduce unnecessary collateral damage [32].
In summary, we observe that for IPv4 many and for IPv6 some HSPs are likely related to blackholing activities due to the used HSP prefix size.
As our CIDR-based analysis only provides us with hints on the actual usage, we now also analyze the services hosted in hyper-specific prefixes.

## Slide 10
Protocols on HSP IPs
We leverage Rapid7’s Open Data platform
Responding hosts and total tested hosts per-protocol
Top5 Protocols:
CWMP is only present in the IPv4-wide
BGP is only present in the HSP
HSPs have upto 5 times higher hitrate than IPv4-wide
Notes: For this analysis, we leverage archived scanning data from Rapid7’s Open Data platform [38] for 2019, 2020, and 2021. Rapid7 frequently scans the entire routed IPv4 address space3 for more than 100 well-known TCP and UDP ports.
To compare regular with hyper-specific prefixes, we rely on the difference in protocol hit rate, i.e., we compare the fraction of responding hosts and total tested hosts4 on a per-protocol basis. We observe that four out of the top five protocols with the highest hit rate for regular and HSP prefixes overlap; BGP is only present in the HSP top five while CWMP is only present in the IPv4-wide top five. For those six protocols, Figure 4 shows a the relative difference of hit rates between regular and hyper-specific prefixes, where a positive value indicates an increase of hit rate in hyper- specific prefixes.
While HTTP and HTTPS overall only see an increase of +100 %, we observe strong differences when drilling down on a per-CIDR level: When considering only /32 prefixes, HTTP’s hit rate increases by more than +500 % compared to its hit rate for IPv4-wide scans—which substan- tiates the association of the /32 CIDR size for blackholing. Even more pronounced than HTTP(S), SMTP and BGP see increases of up to +500%. When digging deeper we further observe that BGP is mainly prevalent in /30 and /29 prefixes, which underlines that these sizes might be dedicated to routing infrastructure. In contrast, we observe the only hit rate decrease (of more than 90%) for CWMP—a protocol used to remotely manage customer-premises equipment (CPE) devices such as home routers

## Slide 11
BGP Communities of HSPs
We examine BGP communites:
specifically used for blackholing (BH)
restrict route propagation (RES)
13% and 7% of IPv4 and IPv6 HSPs are Blackholing
Notes: we investigate BGP communities attached to HSP announcements. BGP communities are used for many different reasons, such as information tagging, blackholing, or route redistribution. The most common BGP communities attached to hyper-specific prefixes are route steering or prepending instructions.
Figure 5 shows the use of BGP communities among HSPs from snapshots between 2019 and 2021. The bars indicate the median share of HSPs with the respective community, the whiskers denote the standard deviation over time.
The “Any” keyword is used to specify groups of community targets, e.g., “Any RES” describes all prefixes that have any restriction community at- tached (i.e., it refers to the union of prefixes with “NO_ADV” community and prefixes with “NO_EXP” communities); similarly, the “Any Comm.” bar refers to the highest aggregation, i.e., prefixes for which we saw any community attached. As we can see, 60% of all IPv4 HSPs and almost three quarters of IPv6 HSPs come with some form of BGP communities. The vast majority of these communities is, however, not related to blackholing or restricting propagation.
Only about 13% and 7% of prefixes can be associated with blackholing for IPv4 and IPv6, respectively. The by far most popular blackholing community is X:666. Moreover, we see no propagation re- striction communities (“no advertise” or “no export”) in IPv6 and only about 0.5% in IPv4.
Furthermore, we see that RES communities are a subset of BH communities, hinting that operators do not want their blackholing prefixes to propa- gate. Blackholing is therefore one contributor of HSPs, but blackholing communities are not present on the majority of HSP announcements.
We note that the blackholing commu- nities that we see at route collector peers is a lower bound: Blackholing communities—similar to other communities— could be cleaned along the path but the prefix itself could continue to propagate
We find concrete evidence for 7–13% of HSPs explicitly tagged with blackholing communi- ties.

## Slide 12
3.INTENDED OR ACCIDENTAL USE?
Notes: Now that we have a basic understanding of the use cases of HSPs, we want to analyze whether HSPs are used intention- ally or accidentally by ASes and their operators. If operators take the time and effort to explicitly enter hyper-specific prefixes into voluntarily-maintained databases, then it is likely that they plan to use them. Hence, we look at the Re- source Public Key Infrastructure (RPKI) and Internet Routing Registry (IRR) operator databases.

## Slide 13
HSPs Origin ASes in Public Databases
IRR has high HSP origin ASes
Many HSPs from RC/BGP have no entries in operator databases
could be accidental announcements
misconfigured route collector sessions
leak of internal routes
Are HSPs caused by BGP prefix hijacks?
Notes: IRR: While this might imply that network operators tend to actually use HSPs, it is well-known that route objects can become stale given that the database is only maintained on a voluntary basis [48]. Yet, some entities, e.g. certain IXP Route Servers [8], require route objects in the IRR database to redistribute prefixes (i.e., HSPs).
Even for the RPKI database we observe hundreds of explicitly defined HSPs6. Notably, for the last snapshot in October 2021, implicit HSPs would have increased the number of RPKI origin ASes from 294 to 990 for IPv4 and from 172 to 794 for IPv6, respectively.
Beyond these intentional HSPs, we also observe that many of the HSPs from Route Collectors have no entries in operator databases, hence, they could potentially represent accidental announcements or misconfigured route collector sessions that leak internal routes.

## Slide 14
HSPs in the RPKI Database
Invalid (Length) - largest group
Invalid (Origin) - a minor fraction
Invalid (Origin) and Invalid (Both):
not entered sibling ASes
DDoS Protection Service (DPS)
legitimate ASes announce 75 % of HSPs
Notes: IRR: While this might imply that network operators tend to actually use HSPs, it is well-known that route objects can become stale given that the database is only maintained on a voluntary basis [48]. Yet, some entities, e.g. certain IXP Route Servers [8], require route objects in the IRR database to redistribute prefixes (i.e., HSPs).
Even for the RPKI database we observe hundreds of explicitly defined HSPs6. Notably, for the last snapshot in October 2021, implicit HSPs would have increased the number of RPKI origin ASes from 294 to 990 for IPv4 and from 172 to 794 for IPv6, respectively.
Beyond these intentional HSPs, we also observe that many of the HSPs from Route Collectors have no entries in operator databases, hence, they could potentially represent accidental announcements or misconfigured route collector sessions that leak internal routes.
We analyze how many hyper-specific prefixes are originated from a DPS as identified by Jin et al. [21] and find that only around 1 % of HSPs in IPv4 and IPv6 are related to DPS companies.
In summary, we observe that for both IPv4 and IPv6, hun- dreds of ASes intentionally entered hyper-specific prefixes into operator databases. Yet we also see that many of the HSPs that are visible from route collectors have no respective entries and are likely related to the accidental announcement or disclosure of internal routes. This is further substantiated by the observation that most HSPs are actually ROV invalid since they are more specific then intended by their covering ROA entry.

## Slide 15
4. THE FUTURE OF HSPS
Notes: Now that we have a basic understanding of the use cases of HSPs, we want to analyze whether HSPs are used intention- ally or accidentally by ASes and their operators. If operators take the time and effort to explicitly enter hyper-specific prefixes into voluntarily-maintained databases, then it is likely that they plan to use them. Hence, we look at the Re- source Public Key Infrastructure (RPKI) and Internet Routing Registry (IRR) operator databases.

## Slide 16
﻿Discussion: Research Community
RC projects play a vital role in awareness
HSP dashboard https://hyperspecifics.io
Notes: While many HSPs seem to be in- tentional, we also observe a large number that potentially represent leaked internal routes. While the task of reconfiguring a leaking router ultimately belongs to the feeder AS’ operators, we believe that the maintainers of route collector projects play a vital role when it comes to raising awareness for the existing problems. To support and guide this process, we publish and maintain a dashboard that provides up-to-date HSP statistics as well as a rankings of the top HSP contributors at https://hyperspecifics.io. Beyond fixing potential leakage errors, we believe that studying the poten- tial correlations between hyper-specific prefixes and their less-specific counter parts may lead to new insights into the routing optimizations used by ASes.

## Slide 17
﻿Discussion: Operator Community
Discussing with thirteen operators
  cutomer requests
  traffic engineering
Question: Should operators filter HSPs in the first place?
  for IPv6, Yes, no shortage of IPv6, avoid large routing table size
  for IPv4, shifting filters by a few CIDR sizes (e.g., /26 or /28)
How do you handle HSPs in your network/work ?
Notes: Even though various guides [11, 12, 29, 33, 34] recommend strict filtering of HSPs, we find that many hyper-specific prefixes propagate to 100 or more collector peers. After discussing our results with thirteen operators from different types of networks, we believe that the limited filtering is often a result of popular customer re- quests. The operator of a major transit network told us that their network recently (throughout Summer 2020) changed from the filtering of all IPv4 HSPs to only filtering prefixes more specific than /28; this shift enabled (especially new and small) customer networks to perform basic traffic engineer- ing despite a limited address allocation7 .
This opens up the question whether operators should filter HSPs in the first place. We believe that for IPv6 the answer is a resounding “yes”. Given that there is no shortage of IPv6 addresses and obtaining new blocks is virtually free (compared to the high costs of obtaining IPv4 addresses), we do not see any reason to loosen the current filtering guidelines. For IPv4, we think that the answer should be more nuanced. While loosening the filtering guidelines allows even small ASes to perform traffic engineering, it would also further increase the routing table size. Hence, we believe that shifting the acceptable boundaries by a few CIDR sizes (e.g., /26 or /28) might be an agreeable compromise.
This opens up the question whether operators should filter HSPs in the first place. We believe that for IPv6 the answer is a resounding “yes”. Given that there is no shortage of IPv6 addresses and obtaining new blocks is virtually free (compared to the high costs of obtaining IPv4 addresses), we do not see any reason to loosen the current filtering guidelines. For IPv4, we think that the answer should be more nuanced. While loosening the filtering guidelines allows even small ASes to perform traffic engineering, it would also further increase the routing table size. Hence, we believe that shifting the acceptable boundaries by a few CIDR sizes (e.g., /26 or /28) might be an agreeable compromise.

## Slide 18
Conclusion
We analyzed HSPs in routing ecosystem for the last decade
Most HSPs visible by a few RC peers, still plenty propagate to hundreds of RC peers
IPv4 HSPs: blackholing and infrastructure announcements
IPv6 HSP: related to address block reassignments
Though, hundreds of networks use HSPs intentionally, we attribute even more cases to the accidental “leakage” of internal routes
HSP dashaboard and the paper
  https://hyperspecifics.io

## Slide 19
Backup Slides
Notes: Over all picture of IPv4 and IPv6
Points:
For Ipv4 Mid 2018 – mid 2019 the number of MSPs has high jumps
  The number of RCs has significantly increased to above 40 RCs – but the number of Feeder Ases not. But we don’t know what is the main reason
    Idea – check the top MSP origin AS per date (Data point)
Mid 2017 is this highes peak for IPv6 MSPs –
  There is not increase in number of RC, with comparison to earlier data point. So why is high ?
    Idea – check the top MSP origin AS per date (Data point)

## Slide 20
Users of HSPs
Comparing all BGP-visible Ases to HSP origin ASes
ISP(Transit) originate more HSPs
12 to 15 of the total 19 Tier 1’s originate HSP
most hypergiants do not originate HSPs
Notes: Furthermore, we see that RES communities are a subset of BH communities, hinting that operators do not want their blackholing prefixes to propagate. Blackholing is therefore one contributor of HSPs, but blackholing communities are not present on the majority of HSP announcements.
We note that the blackholing communities that we see at route collector peers is a lower bound: Blackholing communities—similar to other communities— could be cleaned along the path but the prefix itself could continue to propagate
We find concrete evidence for 7–13% of HSPs explicitly tagged with blackholing communi- ties.

## Slide 21
Growth of HSPs Over Time
presence of HSPs increased
one-tenth of all the prefixes
in IPv4 the increase in HSPs is driven by an increment in feeder ASes
IPv6 we see an increase also for a constant set of feeder ASes
Notes: We observe that the presence of hyper- specific prefixes in the Internet’s routing ecosystem has in- creased through the last decade and HSPs make up about one-tenth of all the prefixes that are observed by route collec- tors. In IPv4 the increase in HSPs is driven by an increment in feeder ASes, whereas in IPv6 we see an increase also for a constant set of feeder ASes. While most HSPs only prop- agate locally, some of them are globally visible and can be consistently observed throughout an entire year.

## Slide 22
HSP Aggregation
Analyse anchor-prefixes:
/24 in IPv4
/48 in IPv6
majority of HSPs are aggregated at the origin – BGP confederation
Notes: ﻿ASes often have economical incentives to keep their BGP routing table size low. To realize this goal, some ASes aggregate (multiple) more-specific routes into a single less-or-equally-specific route
Where does HSP aggregation happen?
For the anchor-prefixes( /24 in IPv4 and /48 in IPv6) we rely on th ATOMIC_AGGREGATE field.
According to RFC 4271 [48], a router MAY set the AGGREGATOR field when it performs prefix-aggregation—which can serve as indication that some form of aggregation must have hap- pened. we rely on th ATOMIC_AGGREGATE field as well as the presence of AS_SET elements in the AS_PATH attribute,
we remove all anchor-routes that contain at least one of them. Where does HSP
Origin and off-path (es- pecially AGGREGATOR fields with private ASNs) aggregation often occurs due to the use of BGP confederations [11, 27] where the AS is internally split into multiple private sub- ASes.

## Slide 23
﻿How Far HSPs Propagate?
Majority of HSPs visible on one peer
  visible on 2+ peers
IPv6 HSPs have better visibility than IPv4 HSPs
Most of HSPs are visible on less than 10 peers
Notes: How visible are HSP? Or How far HSPs propagate?
While we are not able to account this peak to a single factor, we observe that the increase is rather uniform across collector peers, origin ASes, interme- date ASes, and address space and, hence, is unlikely to stem from a measurement artifact or some local misconfiguration.

## Slide 24
HSP Anchors in Various Datasets
Observations:
  Current RC infrastrucure misses 1/3 of anchors potentially contain HSP
  ﻿less noisy, linear increase in the number of anchor prefix for which HSPs
Aggregated class only contains on-path aggregated anchor prefixes
Notes: ROAs for which the most-specific CIDR size would produce an HSP
If the least-specific prefix covered by a ROA is also hyper-specific, we call the ROA explicit; ﻿otherwise, we call the ROA implicit.
We extract all hyper-specific route objects from the “IRR Snapshots“
While our IRR snapshots pro-duced actual HSPs, our final prefix-aggregation and ROAs
only produced a list of anchor-prefixes that is likely to con-tain HSPs.
Notably, some part of this increase can potentially be accounted to the increasing numbers of route collectors and route collector peers over time
We observe the current route collector infrastructure misses roughly one-third of the of the anchor prefixes that potentially contain HSPs?

## Slide 25
HSP Originators Across Datasets
Observations
  HSP origins has more than doubled for IPv4
  ﻿For IPv6, the growth rate of more than 25x
  little overlap between the individual data sets
﻿
Notes: ﻿
For IPv6 the BGP-visible HSP origins grew from a few tens of ASes to about 500 ASes.
For IPv6, the growth rate of more than 25x from 2010 to 2021 is much steeper compared to overall origin ASes.
Given the strong increase in HSP originating ASes, we wonder whether a certain class of ASes is more likely to utilize HSPs.
Comparing this to the growth of all IPv4 and IPv6 ASes, we find that the IPv4 HSP origin growth rate—although impressive—is slower than the overall origin AS growth rate [43]

## Slide 26
Methodology
11+ years (2010-2021)
Supplemental data sets
RPKI Snapshots
IRRs Snapshots
AS Relationships Inferences
AS Classification Inferences
Active Measurement
Passive Measurement
BGP RIBs + updates
From 3 Projects
Advertise our own HSPs to the Internet and contuct experiment.
Route Collectors‘ Data
ASDB
Notes: Resource Public Key Infrastructure (RPKI) Snapshots:
  ROA records to validate the legitimate announcements of prefixes by ASes
Internet Routing Registries (IRRs) Snapshots:
  Records containing route-object information
AS Relationships Inferences (CAIDA)
AS Classification Inferences (CAIDA)

## Slide 27: Cleaning Noisy Data
Rule1:
Misconfigured Peer ASes
Abnormal Prefixes
Private IP ranges
Private Origin ASes
Multicast and IPv4 class E
Rule2:
Testable HSP
For all HSPs, check if it was announced via a route that crossed at least one additional AS then “testable“.
Notes: Rule1:
Misconfigured Peer ASes
Abnormal Prefixes
Private IP ranges
Private Origin ASes
Multicast and IPv4 class E
Rule2:
Testable HSP
For all HSPs, check if it was announced via a route that crossed at least one additional AS then “testable“.
Testable Peer AS
﻿peer AS only then “testable“ if it knows at least ten “testable“ prefixes.

## Slide 28
﻿HSP Propagation Pattern
We use:
AS triplets (three consecutive ﻿ASes) ﻿
AS Relatship Inferences of CAIDA
No single occurrence of P2P relationships
  ASes strongly filter the routes they send to peers
﻿for IPv4 almost all ASes redistribute HSPs “upwards”
  Customers pay their providers to reannounce their prefixes
HSPs are only propagated “vertically” and never “horizontally”.
Notes: all HSPs propagate along the same relationship tuples (green)
at least one HSP propagates along such a relationship tuple(dark-red).
Notably, the ASes in the green bars are distinct from each other while the ASes in the dark-red bars might be counted multiple times (e.g., if they redistribute two HSPs via different relationship tuples).We first observe, that we do not see a single occurrence of P2P relationships, suggesting that ASes strongly filter the routes they send to peers.
for IPv4 almost all ASes redistribute HSPs “upwards”, i.e., they receive the HSP from their customer and announce it to their provider. A
﻿Both of those policies are actually consistent with what we
9One tuple for the first and second AS, one tuple for the second and third AS.
11
heard from various operators: Customers pay their providers to reannounce their prefixes, and so the providers often re- distribute everything they receive from their customers to everyone except their peers.
Finally, we observe that there
is a negligible number of cases where a customer receives
a hyper-specific route from its provider and reannounces it
to another provider. While such cases validate the economic
incentives assumed by the valley-free routing model
Notably, the finding that HSPs are only redistributed “verti-cally” (i.e., from customers to providers and vice versa) and
never “horizontally” is consistent throughout all snapshots
within our observation period.

## Slide 29
Route Collector Data
  ﻿ For our analysis we utilize “snapshots“ from the RC projects Isolario , RIPE RIS , and Routeviews
    From Jan.2010 to October.2021
    Quarterly, 7days per quarter
    BGP RIBs – every 24 hours
    BGP Updates – every 5 mins
  seven-day window allows us to achieve a consistency of 97 % and 98 % for IPv4 and IPv6, respectively.

## Slide 30
﻿Real World Experimentaiton
The PEERING testbed
180 IPv4 and 152 IPv6 neighboring ASes
8 IPv4 and 9 IPv6 neighboring ASes redistributed HSPs
﻿RIPE Atlas probes
﻿To maximize AS coverage - one probe per AS
Experimemt design
﻿prefer dual-stack probes
Highest stable
announce HSP and anchors
wait convergence
run paris-traceroutes from all probes
simultaneously issue ICMP, TCP, and UDP probing
withdraw prefixes
map traceroutes to AS Paths using bdrmapit
﻿IPv4:184.164.240.0/23
Used Prefixes
IPv6:2804:269c:4::/46
Notes: Finally, we want to understand how how much the lack of additional BGP vantage points impacts our observations on reachability?
﻿
we adopt a short an-nouncement cycle: We announce a prefix at the beginning of every full hour and withdraw it 30 minutes later7. We
identify a set of 8 IPv4 and 9 IPv6 neighboring ASes that redistribute HSPs. Notably, those ASes are distributed across 4 and 3 geographically separate Points of Presence.
Technical realization. Throughout May 21 and 22, 2021,
we announce /24, /25, /28, and /32 IPv4 prefixes and /48, /49, /64, /65, /128 prefixes through a single neighbor at the beginning of every even hour. After

## Slide 31
How Far HSPs Propagate?
﻿We did experiment by advertising anchor + HSPs to the Internet
  conduct traceroute from probes
  check it in RC‘s peer ASes
Anchor Prefixes
15% of ASes
The more specific the CIDR size, the less propagation chances.
Current RC‘s infrastructure underestimates data plane reachibility
Notes: As bdrmapit requires a large corpus of traceroutes as input to perform well, we use tracer- oute data from CAIDA’s IPv4 Prefix-Probing data set [69], CAIDA’s IPv4 Routed /24 Topology Dataset [69], CAIDA’s IPv4 Routed /48 Topology Dataset
﻿Comparison. Figure 9 compares the the number of ASes
(aggregated over all iterations) that (1) hosted Atlas probes that reached the target (ATLAS_SOURCE, yellow), (2) appeared along the path between ATLAS_SOURCE ASes and the Peering Testbed (ATLAS_PATH, dark red), (3) are visi- ble from route collector peers (BGP, gray).
Especially for IPv6 we observe that most PEERING neighbors redistribute our prefixes (includ- ing the anchor prefix) only towards their customers, hence, some of our Atlas probes are unable to reach the peering testbed even for the anchor prefix.